## Slide 1: Smoke Tools Workshop
Trent Wickman
trent.wickman@usda.gov
(218) 341-8646

## Slide 2: Who am I?
Native of NE MN and UP of MI
Attended Michigan Tech U
Worked for the State of MN for 5 years as an air permit engineer
Been with Forest Service since 2001
2009 – duties expanded to all the Lake States Forests
2014 – Began doing ARA details

## Slide 3: Review Homework

## Slide 4: Why Should I Care About Smoke?

## Slide 5: What is more important to our health to be clean?
Air
20,000 L/d
Water
1.5 L/d

## Slide 6: Concerns About Smoke???

## Slide 7: Concerns About Smoke
Health: public and firefighters
Safety
Liability
Visibility
Laws and regulations
Nuisance
Social/political
T&E/Wildlife

## Slide 8: Fuels and smoke generation

## Slide 9
Fuel Loading
Fuel Consumption
Emission Factor
Emission Production
Dispersion/Concentration
Largest Error
Second Largest Error
Smallest Error
Black Area

## Slide 10: Combustion and Consumption is Affected by Fuel
Loading
Size
Arrangement
Continuity
Fuel Moisture

## Slide 11: Fuel Moisture Content
Often single most important variable
Live and dead moisture
Increased fuel moisture will generally decrease consumption

## Slide 12: Pre-Ignition Phase
Fuels are heated
Fuel moisture is driven off and water vapor is released
Pyrolysis begins: thermal decomposition of cellulose to combustible vapors

## Slide 13: Flaming Phase
Combustible vapors reach 600° F and mix with sufficient oxygen
Accelerates pyrolysis
Rapid oxidation
Produces primarily CO2 and H2O
Partial oxidation causes a variety of emissions

## Slide 14: Smoldering Phase
Temperature and combustible vapor mixture too low to support flaming
Temperature drops, gases condense
Emissions = 2X flaming stage
Insufficient heat to maintain strong convection column

## Slide 15: Glowing Phase (Residual)
All volatile gases driven off
Carbon remaining
No visible smoke produced
CO2, CO and ash primary products

## Slide 16
Pre
-
ignition
Flaming
Smoldering
Glowing (Residual)
Hot air/gasses
PM
CO
2
PM
2.5
Soot/tar
CO
RX410-8A-16-EP

## Slide 17
PM/SOOT
WATER
TAR
GASES
VAPOR
ASH
Vapors and gases are formed during incomplete combustion and generally cannot be seen.
Soot, tar, and ash are the solid “bits” of particles you can often see formed from chemical reactions in the plume or remnant of flaming combustion.

## Slide 18
Emissions =
Fuel Consumed x Emission Factor
(tons/acre) (pounds/ton)

## Slide 19: Let’s Review - Products of Combustion
Water vapor (H2O)
Carbon dioxide (CO2)
Carbon monoxide (CO)*
Particulate matter (PM)*t
Hydrocarbons (HC) *t
Nitrogen oxide (NOx)*
Secondary emissions (Ozone)*
Primary emissions found in smoke by mass
Perfect Combustion
* = Criteria Pollutants
t = Air Toxics

## Slide 21: Air Quality Regulations

## Slide 22
Cleaner air equals 21 more weeks of life
Thu Jan 22, 2009
By Gene Emery
BOSTON (Reuters) - Dramatic improvements in U.S. air quality over the last two decades have added 21 weeks to the life of the average American, researchers reported on Wednesday.

## Slide 24: EPA Health Standards
NAAQS - National Ambient Air Quality Standards
Set for the 6 “criteria” or common pollutants:
  Particulate matter (PM2.5)
  Ozone (O3), a secondary pollutant
  Carbon Monoxide (CO), Nitrogen Oxides (NOx), Sulfur Dioxide (SO2), Lead (Pb)
Reviewed every 5 years
Enforceable
Exceedances can cause a nonattainment designation

## Slide 25: Particulate Matter
Smoke particles from wood are relatively small
< PM 2.5 microns
PM 2.5-10 microns
> PM 10 microns
70.0%
20.0%
10.0%
RX410-4-25-EP

## Slide 26
From smoke emission to health effects
Particulate matter

## Slide 27
Chart: History of US Particulate Standards
| 1971 | 1987 | 1997 | 2006 | 2012
annual | 75 | 50 | 15 | 15 | 12
24-hr | 260 | 150 | 65 | 35 | 35

## Slide 28: Current NAAQS

## Slide 29: Averaging Time
Standards often have multiple values, each with its own averaging time.
PM2.5 NAAQS =
  Annual average = 12 µg/m3
  24-hr average = 35 µg/m3
KNOW WHAT AVERAGING TIME YOU ARE TALKING ABOUT!

## Slide 31: Exceptional Event Rule
EPA can exclude air quality monitoring data from regulatory determinations related to exceedances/violations of the NAAQS and avoid designating an area as nonattainment if a State adequately demonstrates that an exceptional event has caused the exceedance or violation.

## Slide 32: Key Points of EER
Rx fire may be considered if we provide documentation to support States:
  Fire activity
  Emissions
  Ecological role of specific event
  Proof of compliance with SMP
  Use of basic smoke management practices

## Slide 33: Key Points of EER
  Ecological role of specific event
  What documentation is needed from us?
    FRCC information
    Research on fire ecology for area
    Natural fuels documentation
    Burn not associated with commercial timber operations (clear cut, wind rows, etc.)
    Land/Resource Management Plan, Project NEPA, Burn Plan
    Wildfire versus prescribed fire emissions trade-off

## Slide 34: Key Points of EER
Pre-season collaboration/cooperation with the State is essential to prevent exceedances and address a measured exceedance
Follow Basic Smoke Management Practices or state-specific Smoke Management Plans
Keep important documentation for 3 years

## Slide 35: What Do I Need to Know About Smoke? (cliff notes version)

## Slide 36
Your State Smoke Management Plan
  or Basic Smoke Management Practices if you don’t have a plan
What a Nonattainment Area is and why its bad
  and if you burn in/near one
How to figure out how polluted the air is now
How to predict where my smoke will go (or where it went)
What do I need to know about Smoke? (Cliff Notes version)

## Slide 37: What do I need to know about Smoke? (Cliff Notes version)
Your State Smoke Management Plan
  or Basic Smoke Management Practices if you don’t have a plan
What a Nonattainment Area is and why its bad
  and if you burn in/near one
How to figure out how polluted the air is now
LATER How to predict where my smoke will go (or where it went)

## Slide 38: States with Smoke Management Plans
Alabama
Georgia
Louisiana
S. Carolina
N. Carolina
Virginia
Arkansas
Florida
Mississippi
Illinois*
Minnesota*
Michigan*
Wisconsin?
* = Region 9

## Slide 39: What is the purpose of a SMP?
Minimize smoke entering populated areas (protect public health and sensitive receptors)
Prevent public safety hazards (such as smoke impairment on roadways and runways)
Avoid significant deterioration of air quality and National Ambient Air Quality Standards (NAAQS) violations
Avoid visibility impacts in Class I areas
Process for nuisance mitigation
YOUR PERMIT TO BURN
Notes: SMP captures all the air quality related regulatory requirements in one document. Takes national regulations and any applicable state/local regs and applies to the local situation. ONE SIZE DOES NOT FIT ALL!!
The regulations protect visibility in Class I areas from man-made visibility impairment. Many Class I Areas have fire-dependent veg types, hence smoke is a component of natural visibility in many class I areas. SMP should discuss this. Can you burn a Class I Area? We burn our Class I area.

## Slide 40: Minnesota
Recently updated
No burn by burn authorization

## Slide 41: Sensitive Receptors
Sensitive Receptors—Locations where human population tend to concentrate and where smoke could impact the health of those population or significantly impact visibility that may be detrimental to either health or the enjoyment of scenic qualities of the landscape. These may be residential concentrations in the form of towns or cities, or locations where people tend gather in groups such as parks. Travel routes such as highways may be labeled as sensitive receptor sites where smoke can be a factor in potential motor vehicle accidents. Particular areas along highways or other locations may be more prone to being declared sensitive receptor sites because of topographic and microclimate features.

## Slide 42: Sensitive Receptors
Young
Elderly
Those with cardiovascular or respiratory issues

## Slide 43: Examples
where smoke and air pollutants can adversely affect public health, safety and welfare
population centers such as towns and villages,
campgrounds and trails,
parks
hospitals,
nursing homes,
schools,
roads,
airports,
Class I areas

## Slide 44
4.2.1 Burn Plan Elements
All the organizations burning in Minnesota require prescribed burn plans for each burn. However, if the units are small and the burn objectives and prescription are the same, one plan may cover several burn units. These plans are written following protocols specific to each agency. They will be on file at agency offices and are available upon request. At a minimum, for the purposes of this Smoke Management Plan, these prescribed burn plans must include the following elements:
Location and description of the area to be burned,
Personnel responsible for managing the fire,
Type of vegetation to be burned,
Area (acres) to be burned,
Amount of fuel to be consumed or amount of fuel present on the site (tons/acre),
Fire prescription including smoke management components (see section 4.2.1) and dispersion index,
Criteria the fire manager will use for making burn/no burn decisions,
Safety and contingency plans.
4.2 – Burn Plans

## Slide 45: 4.2.2 Smoke Management Components of Burn Plans
Actions to Minimize Fire Emissions
  Minimize the area burned
  Reduce the fuel loading in the area to be burned by mechanical means or by using frequent, low intensity burns to gradually reduce fuels.
  Reduce the amount of fuel consumed by burning when fuel moistures for 1000 Hour fuels and duff are high.
  Minimize emissions per ton of fuel consumed by using mass ignition techniques, using backing fires, and performing rapid mop-up.

## Slide 46: 4.2.2 Smoke Management Components of Burn Plans
Evaluate Smoke Dispersion
Public Notification and Exposure Reduction Procedures
Air Quality Monitoring

## Slide 47
DI = mixing height x transport wind
The Dispersion Index describes the ability of the atmosphere to disperse
emissions and is the product of the mixing height (ft) and transport wind speed (kts).
4.2.3 - Smoke Management and Dispersion
MH
TW

## Slide 48
4.2.3 - Smoke Management and Dispersion

## Slide 49
4.2.3 - Smoke Management and Dispersion

## Slide 50: Contingency Plan
In burn plan development, include a contingency plan for unexpected smoke impacts.
  This should include a communications plan.
12B-50-Rx410-EP
Notes: VERY important. This is the most overlooked part of the burn plan yet can be the most important. If you get a call in the afternoon that the smoke from your fire is settling into city X, will you know who all to call? Media, schools, elder care facilities, county health dept, etc?? It is best to have thought this out before

## Slide 51: What do I need to know about Smoke? (Cliff Notes version)
Your State Smoke Management Plan
  or Basic Smoke Management Practices if you don’t have a plan
What a Nonattainment Area is and why its bad
  and if you burn in/near one
How to figure out how polluted the air is now
LATER How to predict where my smoke will go (or where it went)

## Slide 53: What do I need to know about Smoke? (Cliff Notes version)
Your State Smoke Management Plan
  or Basic Smoke Management Practices if you don’t have a plan
What a Nonattainment Area is and why its bad
  and if you burn in/near one
How to figure out how polluted the air is now
LATER How to predict where my smoke will go (or where it went)

## Slide 54: EPA’s Air Quality Index (AQI)
Shorter averaging and reporting times
Compiles information on multiple pollutants into one metric
Uses information from continuous monitoring instruments. Some are not “official”
Used for real time communication with the public – easy to understand format
What you hear about in the news

## Slide 55
Index Values | Levels of Health Concern | Cautionary Statements | PM2.5 Breakpoints (µg/m3, 24-hr ave)
0 – 50 | Good | None | 0.0 - 12.0
51 – 100 | Moderate | Unusually sensitive people should consider reducing prolonged or heavy exertion outdoors. | 12.1 - 35.4
101 – 150 | Unhealthy for Sensitive Groups | Active children and adults, and people with lung disease, such as asthma, should reduce prolonged or heavy exertion outdoors. | 35.5 - 55.4
151 – 200 | Unhealthy | Active children and adults, and people with lung disease, such as asthma, should avoid prolonged or heavy exertion outdoors. Everyone else, especially children, should reduce prolonged or heavy exertion outdoors. | 55.5 - 150.4
201 – 300 | Very Unhealthy | Active children and adults, and people with lung disease, such as asthma, should avoid all outdoor exertion. Everyone else, especially children, should avoid prolonged or heavy exertion outdoors. | 150.5 - 250.4
301 – 500 | Hazardous | Everyone should avoid all physical activity outdoors | 250.5 - 500
Notes: The AQI is EPA’s color-coded tool for telling the public how clean or polluted the air is, and steps they
can take to reduce their daily exposure to pollution. The AQI converts concentrations for fine particles to a number on a scale from 0 to 500. The function used to convert from air pollutant concentration to AQI varies by pollutant. If multiple pollutants are measured at a monitoring site, then the largest or "dominant" AQI value is reported for the location.

## Slide 56
https://www.pca.state.mn.us/air/current-air-quality

## Slide 58: EPA Fire and Smoke Map https://fire.airnow.gov/

## Slide 59: BREAK

## Slide 60: Practical Meteorology
Pagami Creek Wildfire, Sept 12th, 2011. Photo by Carl Karasti
7-60-Rx410-EP
Amanda Graning and others….
National Weather Service Duluth, MN

## Slide 61: Dispersion Meteorology Terms
Atmospheric Stability
Lapse Rates
Inversions
Lifting Processes
Mixing Heights
Wind & Wind Shear
Dispersion/Ventilation

## Slide 62: Quick Weather Basics Review

## Slide 63
Atmosphere Cools with Height
The Troposphere

## Slide 64: Atmospheric Stability
The degree to which vertical motion in the atmosphere is enhanced or suppressed
Air warmer than surrounding air rises
Air cooler than surrounding air sinks
7-64-Rx410-EP
Definition:

## Slide 65
Stable Atmosphere
Unstable Atmosphere
Three Types of Stability
Neutral Atmosphere

## Slide 66: Unstable Atmosphere
  Enhances vertical motion
  increases mixing
  increases smoke dispersion
  helps enhance burning
Air parcels
will continue
to rise

## Slide 67: Visual Indicators of Unstable Air
Good visibility
Vertical growth of clouds/Smoke
Cumulus clouds
Gusty winds

## Slide 68: Stable Atmosphere
  suppresses vertical motion
  limits mixing
  limits smoke dispersion
  may require a burn to be shut down

## Slide 69: Visual Indicators of Stable Air
Clouds in layers - No vertical motion
Stratus-type clouds
Smoke column drifts apart after limited rise
Poor visibility in lower levels due to accumulation of smoke and haze
Fog
Light and steady winds

## Slide 70: Weather balloons
Released to sample upper level Temperatures and Winds

## Slide 71: Sounding
Temperature
Pressure/Altitude
Wind Barbs
Dew Point
Temperature
Cloud Base
Tip: Sounding is a vertical weather map
Tip: Think vertical weather map!
Vertical profile of the weather at a point, measured by an instrument called a radiosonde that is released with a weather balloon.

## Slide 72: Inversions
7-72-Rx410-EP

## Slide 73
Positive
Lapse Rate
Inversion!
Recall Lapse Rate…..
Temperature
Height
The change in temperature with increasing altitude
Inversion
Definition:
When temperature increases with increasing altitude.

## Slide 74: Temperature “Inversion”
Temperature
Altitude
Temperature
Inversion
Inversions are stable layers which inhibit upward motion and smoke dispersal.
Form when Warm or Cold air is brought into the Area (advection)

## Slide 75
Four Types of Inversions
6-75-S290-EP

## Slide 76: Formation of Nighttime Inversion
Late afternoon
Evening
Overnight
Sun heats the ground
Ground radiates heat
INVERSION
Altitude

## Slide 77
Ground Absorbs Heat
Altitude
INVERSION
Noon time
Mid morning
Sunrise
Dissipation of Nighttime Inversion

## Slide 78
Mixing
Mixing is a process of upward and downward mixing of a layer of air.
Definition:
Mixing Height
Definition:
The height above ground through mixing occurs. i.e inversion height

## Slide 79: Mixing Height
Temperature
Altitude
Ambient air profile
or sounding
Dry Lapse Rate
Mixing height
Mixing
layer
Mixing Height Varies Through the Day

## Slide 80
Evolution of the
Daytime
Mixing Layer
55ºF
58F
63ºF
75ºF
80ºF
88ºF
8 AM
10 AM
Noon
2 PM
8 AM
1500 Ft AGL
10 AM
2800 FT AGL
Noon
7400 Ft AGL
2 PM
12,000 Ft AGL
Maximum Mixing Height
G r o u n d
6-80-S290-EP

## Slide 81
Seasonal Variation in the Height of the Mixing Layer
The depth of the mixing layer varies considerably during the year.
Average depth of the Mixing Layer
The wildfire is at 2,500 feet ASL.

## Slide 82: Visual Indicators
Low Mixing Height means that smoke concentrates at low levels

## Slide 83: Transport Winds
Temperature
Altitude
Mixing
layer
310 @ 40
330 @ 25
270 @ 10
250 @ 15
230 @ 10
250 @ 12
Average = Transport Winds
Direction Speed
Temperature
Average Winds (direction and speed) in the Mixed Layer; represent net effect of winds that work to move smoke
Definition:

## Slide 84: The stronger the winds The better the dispersion

## Slide 85: Dispersion
Unstable lapse rate (looping)
Stable lapse rate (coning)

## Slide 86
Weather and Smoke Management Forecasts

## Slide 87: Weather and Smoke Mgmt Forecasts.
NWS general, spot and point forecasts provide operational weather information.
www.Weather.gov

## Slide 88: NWS Spot Forecasts
Hysplit??
Notes: All values are automatically generated from the forecast graphics…..recall downfalls of derived hrly temps and wind gusts values...
Can not “Create-and-send” Requires refining by forecaster.

## Slide 89: Smoke Management Forecasts
All NWS offices forecast :
1) Mixing Height
2) Transport Wind
3) Ventilation (dispersion)
4) Haines Index
Text, Graphical and Hourly Forecasts

## Slide 90
Hourly Forecast
for a specific point
Fire Weather Dashboard (Poker)
https://www.weather.gov/dlh/fwd

## Slide 91: LUNCH

## Slide 92: Smoke Tools

## Slide 93: Tool #1) Using Wind Roses to Assess Tradeoffs with Wind Direction Windows

## Slide 94: Tool #2) Using Forecast Soundings to Get a Better Picture of the Smoke Rise and Transport at Your Location

## Slide 95: Tool #3) Using Trajectories to Determine Smoke Transport and Culpability for a Smoke Event

## Slide 96: Trajectory Models
Model that uses archived and/or predicted meteorological info to calculate where air came from (back trajectory) or traveled to (forward trajectory) based on a starting location, height and time.

## Slide 97
Smoke in Minneapolis: Sept 9, 2011
Back trajectory

## Slide 98: What it does NOT do
HYSPLIT trajectory model does NOT produce concentration estimates of smoke.
…meaning it does NOT tell you how MUCH smoke is in the air
…it just tells you WHERE the smoke is going or where it has been

## Slide 99: Key Inputs
Where – Location of fire (smoke)
  X,Y not as important as height AGL (plume rise)
When – when will smoke be generated at a significant height?
Try to bracket possible combinations of conditions (perform multiple runs)

## Slide 100
Chicago Smoke Sept 13, 2011
1700 arrival @ 100 and 1000 m AGL
Noon arrival @ 100 and 1000 m AGL

## Slide 101: Key Issues
Accuracy – model uses gridded meteorological data. Some are 12 x 12 km cells
Not useful for near-field impacts (use spot forecasts of surface and transport wind directions)
A useful tool when used correctly by someone who understands its limitations

## Slide 103
Fuel Loading
Fuel Consumption
Emission Factor
Emission Production
Dispersion/Concentration
Largest Error
Second Largest Error
Smallest Error
Black Area

## Slide 104: Tool # 4) and 5) Dispersion Modeling using Simple Screening and VSMOKE

## Slide 107: Smoke Monitoring – from photos to monitors
Why Monitor?

## Slide 108: Reasons to Monitor
Evaluate impacts on communities
Provide feedback to public, regulators, smoke forecasters, and managers.
Verify assumptions and predictions in analysis documents
Avoid violations of air quality standards.
Assess visibility in Class I areas.

## Slide 109: Reasons to Monitor (cont.)
Wildfire/prescribed fire tradeoffs
Demonstrate we are good neighbors
Establish nuisance thresholds
Distinguish our impacts from others
Verification of predictions from smoke models

## Slide 110: Particulate Monitoring Equipment
Gravimetric
  Filter based; weighs mass
  Labor intensive
  Need line power
  Location semi-permanent
  Very accurate but slow data return
  Not typically used for smoke

## Slide 111: Particulate Monitoring Equipment
Optical
  Measures light scattering or light absorption
  Converts to concentrations
  Real-time data
  Portable
  Relatively inexpensive
  Less accurate than gravimetric
  Used for smoke
PM2.5
E-Sampler

## Slide 112: Particulate Monitoring Equipment
Beta Attenuation Monitors (BAM)
  Collect particulate on a tape
  Radiation is directed across the tape at a sensor
  Tend to be the ones used to produce AQI information
  Smaller version used for smoke
E-BAM

## Slide 113: Cameras
Can incorporate photos with distance markers to gather quantitative data

## Slide 115: Satellite
Issues
Minimum fire size
Cloud cover
Timing of satellite pass

## Slide 116: Where to Monitor
Sensitive locations
  Schools, day care
  Hospitals, nursing homes
  County fairs
Placed away from local pollution sources
  Dirt roads
  Wood stoves
  Traffic
Access to Line Power?
Permission – private property?

## Slide 117: When to Monitor
Depends on objectives
  Project impact monitoring
    May be hourly for several days before and after project
  Permanent network operates year round
    NAAQS monitoring
      Once every six days
    Visibility monitoring
      Every third day

## Slide 118: Nearby Air monitors = FREE data

## Slide 120: Trent’s Smoke Management Program Tips
Establish and maintain relationships with key state air quality folks
Implement an ongoing program to educate the public in likely impacted areas,
  To gain their support for your burning program
  So at-risk folks will remove themselves from dangerous situations
Take existing air quality into account (AQI)
Know your SMP-BSMP/state air regs/procedures
ALWAYS FOLLOW THEM!!
Notes: Don’t want your first introductions to be at an enforcement mtg with the lawyers etc. Invite them out to a burn
Focus message to at-risk populations, young, elderly, cardio/respir conditions
This can’t be our only measure of success/failure – new NAAQS ½ of old
We can’t ignore existing AQ when making go/no-go decisions
If you light up an FRM you better have followed procedure

## Slide 121
http://lakestatesfiresci.net

## Slide 122: Questions?
Feel free to contact me with additional questions

## Slide 123: EXTRAS

## Slide 124: State - Air Monitoring Data
https://www.pca.state.mn.us/air/air-monitoring-network-plan
https://dnr.wisconsin.gov/sites/default/files/topic/AirQuality/2022AnnualNetworkPlan0629.pdf
http://169.62.82.226/documents/egle/ambient-monitoring-network-review-2021-07-01_729037_7.pdf

## Slide 125: Basic Smoke Management Practices
These are good practices to consider whether or not your state has a smoke management plan!
Evaluate Smoke Dispersion Conditions
Monitor Effects on Air Quality
Record-keeping/Maintain a Burn/Smoke Journal
Communication – Public Notification
Consider Emission Reduction Techniques
Share the Airshed – Coordination of Area Burning

## Slide 126: BSMP1: Evaluate smoke dispersion conditions
Before
  Identify smoke sensitive areas
  Identify meteorological conditions
During
  (critical) Obtain latest meteorological forecast
  Obtain AQ conditions (AIRNOW) or state/local
  Verify forecast with observations (RAWS or other)
After, burn operations
  Assess smoldering conditions
Notes: to minimize smoke impacts

## Slide 127: BSMP2: Monitor the effects on air quality
Monitoring effects of fire on air quality
  Where does the smoke go?
  How high does it go?
  Does the smoke disperse or is tight and dense?
Methods – Visual monitoring documented by:
  notes, photographs, aircraft observations, satellite imagery, air quality monitoring data, and post-burn evaluations.
Note air quality near sensitive receptors
US Forest Service Smoke Photo Series
Notes: Monitor the effects of the fire on air quality

## Slide 128: BSMP3: Record-keeping
Keep a personal burn/smoke journal
What records to keep?
  Weather (forecasted and observed)
  BSMPs applied
  Fire activity (location, area burned, date, ignition time, etc.)
  Fuels burned and acreage
  Smoke behavior & impacts (if any)
Assess conditions and burns that meet goals, and provide lessons learned
Documentation can be key if there is an air quality exceedance and the state seeks to exclude the data. This can be years later.

## Slide 129: BSMP 4: Communication – Public Notification
Notify appropriate authorities (e.g., air regulators, public health officials, local fire department)
Notify those in the public potentially affected by the smoke
If an impact occurs, prepare contingency actions to reduce exposure (e.g., mop-up, reducing area burned)

## Slide 130: BSMP5: Consider use of emission reduction techniques (ERTs)
Ensure objectives are not compromised as ERT’s are site specific
ERTs can include:
  reducing fuel burned
  increasing burning efficiency
NRCS Practices considered ERTs: Brush Management, Clearing and Snagging, Firebreak, Forest Stand Improvement, Fuel Break, Prescribed Grazing, and Woody Residue Treatment.

## Slide 131: BSMP6: Share the Airshed – Coordination of Area Burning
Communication among fire managers burning in the same vicinity on the same day
Coordinate and plan ignitions so as not to overwhelm the ability of the atmosphere to disperse the smoke
Current smoke/AQ information
  AIRNOW (http://www.airnow.gov) or from local/state air quality monitoring networks.
  NOAA Hazard Mapping System – current satellite fire detections (http://www.ospo.noaa.gov/Products/land/hms.html )

## Slide 132: Basic Smoke Management Practices
Meteorological scheduling and smoke impact evaluation (critical)
Monitoring effects of the fire on air quality and document smoke dispersion (critical)
Track fire activity on a daily basis
Document the event and retain relevant records for 3.5 years
Share the airshed
Public notification (critical)
Exposure reduction (critical)
Apply emission reduction techniques (ERTs)
http://www.frames.gov/partner-sites/emissions-and-smoke/educational-resources/tutorial/lesson-3/
Notes: Don’t use this slide, use other slide